## Slide 1: BASIC Mechanical Ventilation

## Slide 2: Physics

## Slide 3
FLOW = PRESSURE/RESISTANCE
…..PRESSURE = RESISTANCE X FLOW
Alveolar pressure is divided into 2 components
BASELINE PRESSURE and PRESSURE DUE TO INFLATION OF THE LUNGS
ALVEOLAR PRESSURE = PEEP +VOLUME/COMPLIANCE
Airway pressure, flow and tidal volume are all interlinked.
For any given level of PEEP, only 2 of these 3 variables can be altered.

## Slide 4: OXYGENATION
THE VENTILATOR CAN BE USED TO INCREASE THE ALVEOLAR PARTIAL PRESSURE OF OXYGEN OR TO REDUCE SHUNTING
Fi02
Mean alveolar pressure (mean airway pressure)
Set tidal volume or inspiratory pressure
Inspiratory time
peep
(alveolar ventilation)
Reopening alveoli with increased peep
Prolonged inspiration
INHALED EPOPROSTENOL OR NITRIC OXIDE

## Slide 5: REDUCING CO2
RR
TIDAL VOLUME
Beware barotrauma

## Slide 7: Mechanical Ventilation in 1 Slide…
Negative vs. positive pressure
Pressure vs. volume
Mandatory vs. spontaneous
Oxygenation and ventilation
Don’t forget the heart
Safe rules: Pressures <30cmH2O,
Volumes 8ml/kg,
enough O2 but not too much

## Slide 8: Goals
Patient – ventilator synchrony
Respiratory rate
Respiratory effort
Patient comfort
Prevent ventilator associated lung injury
Flow curves
Pressure Volume loops

## Slide 9: Which Mode?
34 year old 60 kg female
Isolated severe head injury
Paralysed and sedated

## Slide 10: Set the ventilator…..
What are the priorities? (34 year old 60 kg female, isolated severe head injury, Paralysed and sedated)
Tv, Rate (f), FiO2, pressure support (cmH2O),PEEP

## Slide 11
Timing window
Insp Effort Synchronized
with Delivery of Mandatory Vt
Trigger
Level
Spontaneous Breaths
Volume - Synchronized Intermittent Mandatory
Ventilation ( V - SIMV )

## Slide 12
Mandatory Breath
Unsupported
Spontaneous Breaths
Spontaneous Pressure supported Breaths
All Mandatory Breaths Synchronised
to Patients Inspiratory Effort
Volume - Synchronized Intermittent Mandatory
Ventilation ( V - SIMV )

## Slide 13: SIMV (Volume control plus pressure support)
Advantages
  Synchronisation of both mandatory and spontaneous breaths
  Guaranteed minimum minute ventilation
  Rests muscles of respiration (if properly set)
Disadvantages
   lung compliance   alveolar pressure with risk of barotrauma
  Risk of inadequate volumes if pressure limiting
  Inappropriate triggering may result in excessive minute ventilation
  Can still result in excess work of breathing and fatigue.
Notes: The advantages are its relative simplicity, the tidal volume and minimum ventilatory rate are set, thus guaranteeing a minimum minute ventilation and, if properly set, resting the muscles of respiration.
The disadvantages:
Not synchronized with patient’s breathing - ventilator initiated breath may come on top of a patient initiated breath.
Patient may “lead” ventilator (ie try to suck gas out of the ventilator) if inspiratory flow not high enough
Inappropriate triggering (eg as a result of hiccoughs) may result in excessive minute ventilation
Fall in lung compliance results in high alveolar pressure with risk of barotrauma
Often requires sedation to achieve synchrony.

## Slide 14: Initial ABG
pH | 7.31
PaCO2 | 50 mmHg
PaO2 | 412 mmHg
HCO3- | 24
Base excess | +1
Saturation | 100%
Any Changes?
Notes: High PO2 – decrease FiO2
Respiratory acidosis – need to increase alveolar ventilation. Choices are to increase respiratory rate or increase tidal volume or both

## Slide 15: SIMV Summary
Common mode in ICU
Almost invariable for patients returning from theatre
Good for straightforward cases
Bad weaning mode
Bad if problem is oxygenation or poor compliance

## Slide 16: Now which mode?
ICP controlled
  Sedation and paralysis stopped
Patient starts to wake up
Dysynchrony with breath stacking
Notes: The patient improves, the sedation and paralysis is stopped and she start to wake. As she wakes up patient-ventilator dysynchrony develops with breath stacking

## Slide 17
Unsupported Spontaneous Breath
Vt Size
Spontaneous Breath + Pressure Support
Increase in Vt Size
PRESSURE SUPPORT
Spontaneous Insp
Trigger
Vt 200mls
Vt 500mls

## Slide 18: Pressure Support Mode
Primarily a weaning mode
Patient is required to trigger all breaths
Only pressure level is set
All other parameters controlled by patient
Expiration is time cycled
Theoretically more comfortable

## Slide 19: PSV

## Slide 20: Set the ventilator
PEEP, Psp, FiO2
ABG
  pH 7.35
  pCO2 34
  pO2 80
  HCO3 24
  Sats 94%
Happy?
Always assess the patient
Notes: The patient improves, the sedation and paralysis is stopped and she start to wake. As she wakes up patient-ventilator dysynchrony develops with breath stacking

## Slide 21: Pressure support
Advantages
  Simple to set
  Avoids high inspiratory pressures
  Better patient-ventilator synchrony
  Unloads respiratory muscles
  Improved gas flow distribution
Disadvantages
  No apnoea back-up in older ventilators
  Change in lung compliance or resistance  change in tidal volume
  Excessive work of breathing

## Slide 22: Bilevel (Bipap or Duopap) Ventilation
Used to Improve oxygenation or maximise ventilation when compliance is poor.

## Slide 23
FLOW
PRESSURE
INSP
INSP
EXP
EXP
BILEVEL VENTILATION
5
10
15
20
25

## Slide 24: Bilevel Ventilation
Advantages
  Reduces risk of barotrauma
  Improved recruitment of long time constant alveoli
  Patient-ventilator synchrony
Disadvantages
  Overventilation if compliance improves
  Risk of Volutrauma
  Small tidal volumes if pressures are high

## Slide 25: Other settings
Trigger sensitivity
   sensitivity preferable
    Flow triggering general more sensitive than pressure triggering
     flow or  pressure   sensitivity
I:E ratio
Notes: The trigger sensitivity determines how easy it is for the patient to trigger the ventilator to deliver a breath. In general increased sensitivity is preferable in order to improve patient-ventilator synchrony (ie to stop the patient "fighting" the ventilator) but excessively high sensitivity may result in false or auto-triggering (ie ventilator detects what it "thinks" is an attempt by the patient to breath even when the patient is not). Triggering may be flow-triggered or pressure triggered. Flow triggering is generally more sensitive. The smaller the flow or the smaller the negative pressure the more sensitive the trigger

## Slide 26: Other Modes
Assist Control
  Characteristics of each inspiration are the same
  Not affected by whether breath is control breath or an assist breath
CPAP
  PEEP with no pressure support
APRV
  Rescue mode for severe ARDS
Notes: In assist control mode the tidal volume is set. Breaths can either be initiated by the ventilator (control breaths) or by the patient (assist breaths). However, the same tidal volume is delivered in the same time regardless of whether the breath is

## Slide 27: High airway pressure
700 ml
-70
70 l/min
Pressure
Flow
Volume
Pressure alarm limit
Notes: With most ventilators the ventilator inspiration is terminated if the airway pressure reaches the set upper pressure limit. As this usually occurs relatively early in inspiration this results in the patient receiving a much lower tidal volume. This is illustrated on this slide. The first 2 breaths are normal volume control breaths [paw03]
On the subsequent breaths the airway pressure reaches the pressure alarm limit causing the ventilator to terminate inspiration with a resultant fall in airway pressure [paw04] and reduction in tidal volume. [paw05]

## Slide 28: High airway pressure
Significance
  Barotrauma
  Change in patient’s condition
  Inadequate ventilation
Notes: High airway pressure is an important problem because of the risk of barotrauma, because the development of high airway pressure indicates a deterioration in the patient’s condition and because it may lead to inadequate ventilation [paw02]

## Slide 29: Assess
Chest movement
Breath sounds
Respiratory rate
Haemodynamic effects
Oximetry
Blood gases

## Slide 30: Gas Trapping

## Slide 31: Patient ventilator asynchrony

## Slide 32: Man or machine?
Notes: This is most easily determined by disconnecting the patient from the ventilator and manually ventilating him or her. If the problem persists it is a patient or ET tube problem; if it is eliminated it is a ventilator or circuit problem.[urgency04]

## Slide 33: Physics
A (PAW)
B (PALV)
Flow x resistance
Volume/compliance +PEEP
Notes: The airway pressure is determined by flow, volume and PEEP as well as the lung compliance and resistance.

## Slide 34
Notes: or an endobronchial intubation [paw20]

## Slide 35: Questions?