## Slide 1: Haemodynamic Monitoring

## Slide 3: Objectives
Discuss the indications for use of IHM
Describe the insertion sites and techniques
Identify the complications associated with IHM
Interpret IHM pressure waveforms
Describe the nursing care for patients with IHM

## Slide 4: Types of Haemodynamic Monitoring
Non-invasive
  ECG
  Blood Pressure (BP)
  Pulse Oximetry
  Urine Output
Invasive
  Central Venous Catheter
  Arterial Catheter
  Pulmonary Artery Catheter (Swan Ganz)

## Slide 5: Invasive Measures
Central Venous | Arterial | Pulmonary Artery PA pressure and PAWP/PCWP
Central Venous Pressure | Systolic, diastolic and MAP | Pressures of pulmonary artery, and left side of heart

## Slide 6: Arterial Monitoring Indications
Haemodynamic instability
Vasoactive therapy
Acute hypo/hypertensive crisis
Intra and post major surgery
Frequent blood gas samples

## Slide 7: Arterial Measurements
Systolic/Diastolic BP
Mean Arterial Pressure (MAP)
  Average pressure within arterial system
  MAP = systolic + (Diastolic x2)
3
  Average MAP 70-90

## Slide 8: Contraindications
Infection
Haemorrhage
Arterial embolization
Vascular insufficiency

## Slide 9: Allen’s test

## Slide 10: Radial insertion

## Slide 11: Monitoring System Components

## Slide 12: Accurate arterial pressure measurement
Pressure bag inflated to 300mmHG
Transducer position – phlebostatic axis
Zeroing the transducer
Correlate to other BP measurements

## Slide 13
Phlebostatic Axis – 4th intercostal space, midaxilla.

## Slide 14: Ensuring Accuracy
ZEROING’
Eliminates atmospheric influence on pressure readings
Open transducer to air and “zero”

## Slide 15: Square Wave Testing

## Slide 16: Interpreting the Arterial Waveform
Notes: Systole goes from end of diastole, until diacrotic notch
Top of the wave form = peak to systolic pressure (L vent contraction)
On downward stroke, the notch (diacrotic)= closure of aortic valve (retrograde bld flow). This is the point were systole finishes and diastole starts.
End distolic pressure is the lowest point = opening of aortic valve.
Pulse pressure- the difference between your systolic and diastolic blood pressure measurements. A very large pulse pressure indicates higher risk for heart problem
Diacrotic notch should be 1/3 or greater of the height of systolic peak otherwise suspect reduced cardiac output.

## Slide 17
Notes: Normal arterial wave form in relation to ECG

## Slide 18
Notes: Can learn alot from arterial trace - amount of perfusion ectopics produce compared to normal SR conducted beats
- affect AF is having on perfusion
- is your ECG trace actually PEA (ie. Do you actually have an output?!)
- do you have mechanical capture as well as electrical capture (re: testing pacing)
- VAD has no waveform – just MAP reading as non pulsatile blood flow.

## Slide 19: Mechanical Problems
Over-dampening
Under-dampened
No Waveform

## Slide 20: Mechanical Problems

## Slide 21: Dampening
    Air bubbles
    Thrombus
    Catheter on vessel wall
    Catheter kinked/knotted
    Loose connection
    Incorrect calibration

## Slide 22: No Waveform
    Leak in system
    Loose/cracked transducer
    Air in transducer
    Stopcock wrong way
    Lumen clotted
    Pressure in bag low
    Defective transducer

## Slide 23: Nursing Care
Monitor neurovascular status
Maintain aseptic technique
Prevent complications

## Slide 24: Neurovascular Status
NV assessment of distal limb hourly
Splint / support / suture to prevent arterial spasm / thrombosis / haematoma
Flush tubing after taking blood
Assess for nerve damage

## Slide 25: Aseptic Technique
Wash hands
Aseptic technique
Change IV transducer set every 72 hours
Redress 3rd daily and prn
Inform MO if been insitu for 7 days

## Slide 26: Complications
Vascular thrombosis
Embolism
Vascular spasm
Necrosis at site
Peripheral ischemia
Haemorrhage
Anemia
Blood test errors
Local infection
Systemic infection
Nerve damage
Inadvertent drug administration
Notes: Picture of inadvertent drug administration https://seattleclouds.com/myapplications/dukeg/ican/ArtLine.html

## Slide 27
Notes: Necrosis process from infection and microemboli – actual patient
Top pic is debrided wound.

## Slide 28: Prevent Complications
Ensure correct line labelling
Cannula secure
Line visible
Connections secure
Monitor neurovascular status and record phlebitis score
Red cap over access port

## Slide 29: Central Venous Pressure (CVP)
Also known as right atrial pressure (RAP)

## Slide 30: CVL Insertion Primary Indications
To monitor volume status
Guide administration of fluids and electrolytes
To monitor right ventricular function
Parenteral nutrition
Drug Therapy
Lack of accessible peripheral veins

## Slide 31: CVP Monitoring
Direct measurement of the pressure of the right atrium
Measured from the superior or inferior vena cava as there are no valves
Represents the volume of blood within the RA
It can be measured continuously via a pressure transducer or intermittently via a water manometer

## Slide 32: Central Venous Pressure Monitoring
Tip of the catheter is positioned in a central vein, usually the superior vena cava
Reflects right sided heart function
Notes: CVP is the pressure of the blood emptying into the right ventricle during diastole
Directly measures the pressure in the superior vena cava = CVP
The superior vena cava openly communicates with the right atrium and measure RAP.
Preload for the R) ventricle

## Slide 33: CVP Monitoring
CVP measurement is read from the distal lumen of CVC
Normal 0-8 mmHg (3-11cm H20)
Notes: Position of CVP monitoring – emphasise brown lumen (show positioning via flushing – can also show reason not to use smaller syringes)
Monitoring should be attached to 3wt with hydration for emergency access.

## Slide 34: Obtaining CVP Measurement
Position pt supine or HOB up to 30 degrees
Move transducer to the phlebostatic axis. What is the significance of this landmark?
Check patency of intravenous line prior to pressure measurement by flushing line.
Zero transducer to atmospheric pressure.
Notes: If using water manometer - Level water manometer to.
Mark this point on the pt’s skin to ensure consistency in technique from shift to shift.

## Slide 35: Normal CVP wave form
Notes: The CVP reading is taken at the last half of the A wave at the midpoint of the X descent
Explain graph by starting at v wave and working through; atrial filling, tricuspud valve open, atrial kick (30% CO), atrial relaxation, bulging of tricuspid valve during ventricular systole.

## Slide 36: Causes of Low CVP
Hypovolaemia
Profound vasodilation
Any other condition that reduces venous return to the heart

## Slide 37: Causes of High CVP
Intra-vascular volume overload
Right ventricular failure
Anything that increases pre-load or
after-load
Decreased contractility

## Slide 38: Complications of insertion
Notes: Frontal chest radiograph shows a left-sided pneumothorax following insertion of a central venous catheter. Note that the subclavian approach (arrow) was used for insertion of the catheter

## Slide 39: Central Venous Complications
IMMEDIATE
Bleeding
Arterial puncture
Arrhythmia
Air embolism
Catheter malposition
Pneumothorax or haemothorax
DELAYED
Infection
Venous thrombosis, pulmonary emboli
Catheter migration
Catheter embolization
Myocardial perforation
Nerve Injury

## Slide 40: Haemodynamic Monitor
Notes: Art – systolic is highest measurement after QRS
CVP – lowest point just after QRS (systole) and

## Slide 41: Key points for accurate measurements
Levelling to Phlebostatic Axis
Positioning of Transducer
Zeroing with every change of patient position

## Slide 42: Decision Making
Therapeutic judgements & decisions are best based on monitoring & clinically observed changes over time…& not an isolated measurement
Look at clinical picture of patient!!

## Slide 43: Questions

## Slide 44: Summary
Invasive pressure monitoring provides a accurate measurement of a patient’s haemodynamic status
We need to remain aware of potential complications and assess our patient regularly